## Slide 1
Wireless Network Security
Module 07
Notes: 1549496762

## Slide 2
Module Objectives
Understanding the Wireless Terminology, Wireless Networks, and Wireless Standards
Understanding the Wireless Network Topologies and Classification of Wireless Networks
Understanding the Components of a Wireless Network
Overview of Wireless Network Encryption Mechanisms
Understanding Wireless Network Security Measures and Wireless Security Tools
Understanding the Different Types of Wireless Network Authentication Methods
1
2
3
4
5
6

## Slide 3
Understand Wireless Network Fundamentals
Understand Wireless Network Encryption Mechanisms
Discuss Different Types of Wireless Network Authentication Methods
Discuss and Implement Wireless Network Security Measures
Module Flow
01
02
03
04

## Slide 4
Bandwidth
Describes the amount of information that may be broadcast over a connection
BSSID
The MAC address of an AP that has set up a Basic Service Set (BSS)
Hotspot
A place where a wireless network is available for public use
ISM band
A set of frequencies for the international industrial, scientific, and medical communities
Access point (AP)
Used to connect wireless devices to a wireless/wired network
GSM
A universal system used for mobile transportation for wireless networks worldwide
Wireless Terminologies

## Slide 5
Wireless Terminologies (Cont’d)
Service Set Identifier (SSID)
A unique identifier of 32 alphanumeric characters given to a wireless local area network (WLAN)
Orthogonal Frequency-division Multiplexing (OFDM)
Method of encoding digital data on multiple carrier frequencies
Multiple input, multiple output orthogonal frequency-division multiplexing (MIMO-OFDM)
An air interface for 4G and 5G broadband wireless communications
Direct-sequence Spread Spectrum (DSSS)
An original data signal multiplied with a pseudo-random noise spreading the code
Frequency-hopping Spread Spectrum (FHSS)
A method of transmitting radio signals by rapidly switching a carrier among many frequency channels
Association
The process of connecting a wireless device to an AP

## Slide 6
Wireless Networks
Advantages
Wireless networks use radio frequency (RF) signals to connect wireless-enabled devices in a network
The wireless fidelity (Wi-Fi) technology uses the Institute of Electrical and Electronics Engineers (IEEE) standard of 802.11 and uses radio waves for communication
Installation is easy and eliminates wiring
Access to the network can be from anywhere within the range of an access point (AP)
Public places such as airports, schools, etc., can offer a constant internet connection using WLAN

## Slide 7
Wireless Technologies
It uses long distance wireless networking and high-speed Internet and belongs to the IEEE 802.16 family of wireless networking standards
WiMAX
Wi-Fi
Using Bluetooth technology, data is transmitted between cell phones, computers, and other networking devices over short distances
Bluetooth
It uses radio frequency (RF) electromagnetic waves to transfer data for automatic identification and for tracking tags attached to objects
RFID
In a wireless network, data transmission occurs by means of electromagnetic waves that carry signals over the communication path
Types of Wireless Technologies
It uses radio waves or microwaves to allow electronic devices to exchange data or connect to the Internet

## Slide 8
Wired vs. Wireless Networks
Wired Networks | Wireless Networks
High bandwidth | Low bandwidth
Low bandwidth variation | High bandwidth variation
Low error rates | High error rates
More secure | Less secure
Less equipment dependent | More equipment dependent
Symmetric connectivity | Possible asymmetric connectivity
High-power machines | Low-power machines
High-resource machines | Low-resource machines
Low delay | High delay
Connected operation | Disconnected operation

## Slide 9
Wireless Standards
Protocol | Frequency (GHz) | Bandwidth (MHz) | Stream data rate (Mbits/s) | Modulation | Range (m) | 
 |  |  |  |  | Indoor | Outdoor
802.11 (Wi-Fi) | 2.4 | 22 | 1, 2 | DSSS, FHSS | 20 | 100
802.11a | 5 | 20 | 6, 9, 12, 18, 24, 36, 48, 54 | OFDM | 35 | 120
 | 3.7 |  |  |  |  | 
 |  |  |  |  | — | 5000
802.11b | 2.4 | 22 | 1, 2, 5.5, 11 | DSSS | 35 | 140
802.11d | It is an enhanced version of 802.11a and 802.11b that enables global portability by allowing variation in frequencies, power levels, and bandwidth |  |  |  |  | 
802.11e | It provides guidance for prioritization of data, voice, and video transmissions by enabling quality of service (QoS) |  |  |  |  | 
802.11g | 2.4 | 20 | 6, 9, 12, 18, 24, 36, 48, 54 | OFDM |  | 

## Slide 10
Wireless Standards (Cont’d)
Protocol | Frequency (GHz) | Bandwidth (MHz) | Stream data rate (Mbits/s) | Modulation | Range (m) | 
 |  |  |  |  | Indoor | Outdoor
802.11i | This is a standard for WLANs that provides improved encryption for networks that use the 802.11a, 802.11b, and 802.11g standards |  |  |  |  | 
802.11n | 5 | 20 | 7.2, 14.4, 21.7, 28.9, 43.3, 57.8, 65, 72.2 | MIMO-OFDM | 70 | 150
 | 2.4 | 40 | 15, 30, 45, 60, 90, 120, 135, 150 |  | 70 | 150
802.11ac | 5 | 20 | 7.2, 14.4, 21.7, 28.9, 43.3, 57.8, 65, 72.2, 86.7, 96.3 | MIMO-OFDM | 35 | 
 |  | 40 | 15, 30, 45, 60, 90, 120, 135, 150, 180, 200 |  | 35 | 
 |  | 80 | 32.5, 65, 97.5, 130, 195, 260, 292.5, 325, 390, 433.3 |  | 35 | 
 |  | 160 | 65, 130, 195, 260, 390, 520, 585, 650, 780, 866.7 |  | 35 | 
802.11ax | 2.4/5/6 | 40 | Up to 2294[F] | MIMO-OFDM | 30 | 120
 |  | 80 | Up to 4803[F] |  |  | 
 |  | 80+80 | Up to 10530 |  |  | 

## Slide 11: Wireless Standards (Cont’d)
Protocol | Frequency (GHz) | Bandwidth (MHz) | Stream data rate (Mbits/s) | Modulation | Range (m) | 
 |  |  |  |  | Indoor | Outdoor
802.11ad | 60 | 2160 | 6.75 Gbit/s | OFDM, single carrier, low-power single carrier | 60 | 100
802.12 | This standard defines the demand priority and media access control protocol for increasing the Ethernet data rate to 100 Mbps |  |  |  |  | 
802.15 | This standard defines the communication specifications for wireless personal area networks (WPANs) |  |  |  |  | 
802.15.1 (Bluetooth) | 2.4 |  | 1-3 Mbps |  | 10 | 
802.15.4 (Zigbee) | 2.4 | 868, 900 |  |  |  | 
802.15.5 | A standard for mesh networks with enhanced reliability via route redundancy |  |  |  |  | 
802.16 | A group of broadband wireless communication standards for metropolitan area networks (MANs) |  |  |  |  | 

## Slide 12
Wireless Network Topologies
  Ad-hoc Standalone Network Architecture (Independent Basic Service Set (IBSS))
Devices exchange information with each other similar to that in a peer-to-peer communication mode without the need of an AP for communication
To setup this mode properly, first configure the wireless adapter for all the devices. They should all have the same channel name and SSID in order to activate the connections
  Infrastructure Network Topology (Centrally Coordinated Architecture/ Basic Service Set (BSS))
Devices in the wireless network are connected through an AP
An AP connects to the internet via a modem
Installed in large organizations

## Slide 13
  Wireless Networks Based on the Connection
Classification of Wireless Networks
  Extension to a Wired Network
  Multiple Access Points
  LAN-to-LAN Wireless Network
  4G Hotspot
Internet
Broadband Router
Users
Users
Access Point
Extension Point
Internet
Broadband Router
Users
Access Point
Access Point
Users
Users
Cell Tower
3G Hotspot
Internet
3G Connection
3G/4G USB
Broadband Router
Broadband Router
LAN 1
LAN 2

## Slide 14
Classification of Wireless Networks (Cont’d)
WLAN
  It connects users in a local area with a network. The area may range from a single room to an entire campus
WWAN
WWAN covers an area larger than the WLAN. It can cover a particular region, nation, or even the entire globe
WPAN
It interconnects devices positioned around an individual, in which the connections are wireless. It has a very short range
WMAN
It accesses broadband area networks by using an exterior antenna. It is a good alternative for a fixed-line network
  Wireless Network Based on the Geographic Area Coverage

## Slide 15
Components of a Wireless Network
Access Point (AP)
  It is a hardware device that allows wireless communication devices to connect to a wireless network via wireless standards such as Bluetooth, Wi-Fi, etc.
Wireless Cards (NIC)
  Systems connected to the wireless network require a network interface cards (NIC) to establish a standard Ethernet connection
Wireless Modem
It is a device that receives and transmits network signals to other units without requiring physical cabling
Wireless Bridge
It connects multiple LANs at the medium access control (MAC) layer and is separated either logically or physically. It is used for increasing the coverage area of the wireless network

## Slide 16
Components of a Wireless Network (Cont’d)
Wireless Repeater
  Retransmits the existing signal captured from a wireless router or AP to create a new network
Wireless Router
  Performs the functions of a router as well as a wireless AP and provides Internet access to various devices
Wireless Gateways
  Routes data packets and functions as a wireless AP. An Internet connection can be shared between multiple stations
Wireless USB Adapter
Connects different devices to a wireless network in order to access the Internet without a computer, router, or any other network device

## Slide 17
Components of a Wireless Network (Cont’d)
Directional Antenna
Omnidirectional Antenna
Yagi Antenna
Used for broadcasting and obtaining radio waves from a single direction
It is based on the principle of a satellite dish and can pick up Wi-Fi signals from a distance of 16 km or more.
Bidirectional antenna, used for supporting client connections rather than site-to-site applications
It provides a 360° horizontal radiation pattern. It is used in wireless base stations.
A unidirectional antenna commonly used in communications in the frequency band from 10 MHz to very high frequency (VHF) and ultra high frequency (UHF)
These are used for concentrating electromagnetic energy that is radiated or received at a focal point
  Types of Antenna
Antenna
  Converts electrical impulses into radio waves and vice versa
Dipole Antenna
Reflector Antennas
Parabolic Grid Antenna

## Slide 18
Understand Wireless Network Fundamentals
Understand Wireless Network Encryption Mechanisms
Discuss Different Types of Wireless Network Authentication Methods
Discuss and Implement Wireless Network Security Measures
01
02
03
04
Module Flow

## Slide 19
Types of Wireless Encryption
802.11i
WEP
EAP
LEAP
WPA
TKIP
An IEEE amendment that specifies security mechanisms for 802.11 wireless networks
An encryption algorithm for IEEE 802.11 wireless networks
Supports multiple authentication methods, such as token cards, Kerberos, and certificates
A proprietary version of EAP developed by Cisco
An advanced wireless encryption protocol using TKIP and MIC to provide stronger encryption and authentication
A security protocol used in WPA as a replacement for WEP

## Slide 20
Types of Wireless Encryption (Cont’d)
WPA2
An upgrade to WPA using AES and CCMP for wireless data encryption
AES
A symmetric-key encryption, used in WPA2 as a replacement for TKIP
An encryption protocol used in WPA2 for stronger encryption and authentication
CCMP
Integrates EAP standards with WPA2 encryption
WPA2 Enterprise
A centralized authentication and authorization management system
RADIUS
A protocol that encapsulates the EAP within an encrypted and authenticated transport layer security (TLS) tunnel
PEAP
A third-generation Wi-Fi security protocol that uses GCMP-256 for encryption and HMAC-SHA-384 for authentication
WPA3

## Slide 21
Wired Equivalent Privacy (WEP) Encryption
-
-
WEP Key Store (K1, K2, K3, K4)
WEP Seed
WEP-encrypted Packet (Frame body of MAC Frame)
CRC-32 Checksum
Keystream
RC4 Cipher
XOR Algorithm
X
WEP Key
IV
Data
ICV
IV
PAD
KID
Ciphertext
WEP is a security protocol defined by the 802.11b standard; it was designed to provide a wireless LAN with a level of security and privacy comparable to that of a wired LAN
WEP uses a 24-bit initialization vector (IV) to form stream cipher RC4 for confidentiality and the CRC-32 checksum for integrity of wireless transmissions
It has significant vulnerabilities and design flaws and can therefore be easily cracked
How WEP Works

## Slide 22
Wi-Fi Protected Access (WPA) Encryption
Data to Transmit
Key Mixing
WEP seed
MSDU
MIC key
MPDU
ICV
XOR Algorithm
Packet to transmit
MSDU + MIC
Keystream
Michael Algorithm
Fragmen-tation
X
Transmit Address
TSC (IV + EIV)
Mac Header
Ciphertext
IV
KID
EIV
CRC-32
Check
sum
Temporal Encryption Key
RC4
Cipher
How WPA Works
WPA is a security protocol defined by 802.11i standards; it uses a Temporal Key Integrity Protocol (TKIP) that utilizes the RC4 stream cipher encryption with 128-bit keys and 64-bit MIC integrity check to provide stronger encryption and authentication
WPA uses TKIP to eliminate the weaknesses of WEP by including per-packet mixing functions, message integrity checks, extended initialization vectors, and re-keying mechanisms

## Slide 23
WPA2 Encryption
WPA2-Enterprise
WPA2-Personal
How WPA2 Works
MAC Header
CCMP Header
Encrypted MIC
MAC Header
PN
Priority destination address
Build AAD
Build Nonce
AAD
Nonce
Temporal Key
AES CCMP
WPA2 MAC Frame
Plaintext Data
Encrypted Data
Build CCMP header
Modes of Operation
  It uses a set-up password (pre-shared Key, PSK) to protect unauthorized network accesses
  In PSK mode, each wireless network device encrypts the network traffic using a 128-bit key, which is derived from a passphrase of 8 to 63 ASCII characters
  It includes EAP or RADIUS for centralized client authentication using multiple authentication methods, such as token cards, and Kerberos
  Users are assigned login credentials by a centralized server, which they must present when connecting to the network
WPA2 is an upgrade to WPA, and it includes mandatory support for counter mode with cipher block chaining message authentication code protocol (CCMP), an AES-based encryption mode with strong security

## Slide 24
WPA3 Encryption
  WPA3 - Personal
WPA3 - Enterprise
WPA3 is an advanced implementation of WPA2 providing trailblazing protocols and uses the AES-GCMP 256 encryption algorithm
  It is mainly used to deliver password-based authentication using the SAE protocol, also known as Dragonfly Key Exchange
  It is resistant to offline dictionary attacks and key recovery attacks
It protects sensitive data using many cryptographic algorithms
It provides authenticated encryption using GCMP-256
It uses HMAC-SHA-384 to generate cryptographic keys
It uses ECDSA-384 for exchanging keys
Modes of Operation

## Slide 25
Encryption | Attributes |  |  |  | 
 | Encryption Algorithm | IV Size | Encryption Key Length | Key Management | Integrity Check Mechanism
WEP | RC4 | 24-bits | 40/104-bits | None | CRC-32
WPA | RC4, TKIP | 48-bits | 128-bits | 4-way handshake | Michael algorithm and CRC-32
WPA2 | AES-CCMP | 48-bits | 128-bits | 4-way handshake | CBC-MAC
WPA3 | AES-GCMP 256 | Arbitrary length 1 - 264 | 192-bits | ECDH and ECDSA | BIP-GMAC-256
WEP, WPA | Should be replaced with more secure WPA and WPA2
WPA2 | Incorporates protection against forgery and replay attacks
WPA3 | Provides enhanced password protection and secured IoT connections; encompasses stronger encryption techniques
Comparison of WEP, WPA, WPA2, and WPA3

## Slide 26
Issues in WEP
Issues in WPA
Issues in WPA2
Issues in WEP, WPA, and WPA2
  CRC-32 does not ensure complete cryptographic integrity
  IVs are 24 bits and sent in cleartext
  Vulnerable to known plaintext attacks
  Prone to password cracking attacks
  Lack of centralized key management
  Pre-shared key is vulnerable to eavesdropping and dictionary attacks
  Lack of forward secrecy
  WPA-TKIP is vulnerable to packet spoofing and decryption attacks
  Insecure random number generator (RNG) in WPA allows the discover of GTK generated by AP
  Vulnerabilities in TKIP allow attackers to guess the IP address of the subnet
  Pre-shared key is vulnerable to eavesdropping and dictionary attacks
  Lack of forward secrecy
  Hole96 vulnerability makes WPA2 vulnerable to MITM and DoS attacks
  Insecure random number generator (RNG) in WPA2 allow attackers to discover GTK generated by AP
  KRACK vulnerabilities make WPA2 vulnerable to packet sniffing, connection hijacking, malware injection, and decryption attacks

## Slide 27
Understand Wireless Network Fundamentals
Understand Wireless Network Encryption Mechanisms
Discuss Different Types of Wireless Network Authentication Methods
Discuss and Implement Wireless Network Security Measures
01
02
03
04
Module Flow

## Slide 28
Wi-Fi Authentication Methods: Open System Authentication
Any wireless device can be authenticated with the AP, thus allowing the device to transmit data only when its WEP key matches to that of the AP
Client attempting to connect
Switch or Cable Modem
Internet
Access Point (AP)
Probe request
Probe response (security parameters)
Open system authentication request
Open system authentication response
Association request (security parameters)
Association response

## Slide 29
Wi-Fi Authentication Methods: Shared Key Authentication
The station and AP use the same WEP key to provide authentication, which means that this key should be enabled and configured manually on both the AP and client
Client attempting to connect
Switch or Cable Modem
Internet
Access Point (AP)
Client encrypts challenge text and sends it back to AP
AP sends challenge text
Authentication request sent to AP
Client connects to network
AP decrypts challenge text, and if correct, authenticates client

## Slide 30
Wi-Fi Authentication Process Using a Centralized Authentication Server
Client
AP sends an EAP-Request to determine identity
Client requests connection
EAP-Response with identity
Access Point
RADIUS Server
Forwards the identity to the RADIUS server using the uncontrolled port
Sends a request to the wireless client via the AP specifying the authentication mechanism to be used
The wireless client responds to the RADIUS server with its credentials via the AP
Sends an encrypted authentication key to the AP if the credentials are acceptable
Sends a multicast/global authentication key encrypted with a per-station unicast session key

## Slide 31
Understand Wireless Network Fundamentals
Understand Wireless Network Encryption Mechanisms
Discuss Different Types of Wireless Network Authentication Methods
Discuss and Implement Wireless Network Security Measures
01
02
03
04
Module Flow

## Slide 32
Wireless Network Security Measures
01
Create an inventory of wireless devices
05
Defend against WPA cracking
02
Placement of the wireless AP and antenna
06
Detect rogue APs
03
Disable SSID broadcasting
07
Locate rogue APs
04
Select a strong wireless encryption mode
08
Configure the security on wireless routers
  Wireless Network Security Techniques

## Slide 33
https://www.acrylicwifi.com
Creating an Inventory of Wireless Devices
# | Make | Model | Operating System | Strongest Authentication Mode | Best Firmware Level | 802.11 Radio Type | Maximum Output Power
A | Intermec | CK31 | Win CE .NET | WPA2/802.1x | 4.20 | b/g | 17 dBm
B | Symbol | 9090G | Windows Mobile | WPA2/802.1x | 5.1.70 | a/b/g | 20 dBm
C | Vocollect | Talkman T5 | Proprietary Voice | WPA-PSK | 4.20 | b only | 12 dBm
D | Symbol | 6846 | MS-DOS | WEP | - | b only | 20 dBm
E | XybernautAtigo | S310LX | Windows XP | WPA2/802.1x | 5.0 | a/b/g | 20 dBm
Identify and document all the client devices according to the make/models/applications, encryption, firmware, wireless channel, etc.
This helps the network defenders to manage and monitor the wireless devices in the network

## Slide 34
Guidelines for AP mounting:
  Place APs in central locations
  Install an AP on the ceiling
  Avoid placing APs too high on ceilings
  Avoid mounting an AP on a wall as it may restricts its 360° coverage
  Avoid installing APs in corridors
  Avoid installing APs above suspended ceilings
  Use locks and a plastic sarel enclosure to secure the AP from theft
  Avoid enclosing the AP in a metal cage
  Keep the AP away from metal objects
Placement of a Wireless AP

## Slide 35
Placement of a Wireless Antenna
  Guidelines for antenna placement:
    Use the trial-and-error method to select an appropriate location and direction
    Place the AP antenna in a perpendicular direction
  Avoid keeping the antenna at an angle of 45°
  Point the antenna gain towards users
  Know the antenna radiation patterns
  Do not place obstructions or objects that interfere with the function of the antenna
  The use of external antennas as integrated antennas has a limitation

## Slide 36
Disable SSID Broadcasting
If the SSID is broadcast, the AP will announce its presence and name, allowing everyone to attempt to authenticate and connect to the wireless network
The SSID broadcast should be disabled. In this scenario, an AP will only broadcast its presence, but not its name.
This discourages unauthorized association requests to the network and permits connections from legitimate users to the wireless network who have the correct SSID

## Slide 37
01
02
03
04
05
06
07
Selecting a Strong Wireless Encryption Mode
A strong wireless encryption mode should be selected for the wireless network
Order of preference for choosing an encryption mode:
WPA3
  WPA2 Enterprise with RADIUS
  WPA2 Enterprise
  WPA2 PSK
  WPA Enterprise
  WPA
  WEP

## Slide 38
Defending Against WPA Cracking
Select a random passphrase that is not made up of dictionary words
Select a complex passphrase which contains a minimum of 20 characters and change the passphrase at regular intervals
Use a virtual private network (VPN) such as a remote access VPN, Extranet VPN, Intranet VPN, etc.
Use WPA3 /WAP2 encryption only
Set the client settings properly (e.g., validate the server, specify the server address, do not prompt for new servers, etc.)
Implement a network access control (NAC) or network access protection (NAP) solution for additional control over end-user connectivity

## Slide 39
Detecting Rogue Access Points
Wireless Scanning
Wired Network Scanning
Simple Network Management Protocol (SNMP) Polling
Performs a wireless network scanning to detect the presence of wireless APs in the vicinity
  Discovery of an AP not listed in the wireless device inventory indicates the presence of a rogue AP
  Use wireless discovery tools such as inSSIDer, NetSurveyor, NetStumbler, Vistumbler, Kismet, etc., to detect wireless networks
Use network scanners such as Nmap to identify APs on the network. This will help in locating rogue devices on the wired network
Use the SNMP to identify the IP devices attached to the wired network
Use the SNMP detection utilities such as SolarWinds SNMP scanner, Lansweeper SNMP scanner, etc., to identify the SNMP-enabled devices on the network
Note: To use SNMP polling, the SNMP service on all IP devices in the network should be enabled.

## Slide 40
Wireless Security Tools
https://sourceforge.net
Cisco Adaptive Wireless IPS
https://www.cisco.com
It provides wireless-network threat detection and mitigation against malicious attacks and security vulnerabilities
AirMagnet WiFi Analyzer PRO
https://www.netally.com
RFProtect
https://www.arubanetworks.com
Fern Wifi Cracker
https://github.com
OSWA-Assistant http://securitystartshere.org
BoopSuite https://github.com

## Slide 41
Configuring the Administrative Security on Wireless Routers
Change the default password on the wireless router
Assign a strong and complex password to the router
Choose the HTTPS for secure communication
Disable remote router access
Enable logging

## Slide 42: Configuring the Administrative Security on Wireless Routers (Cont’d)

## Slide 43
This module has discussed the wireless terminology, wireless networks, and wireless standards
1
2
It also discussed the wireless network topologies and classification of wireless networks
3
This module has discussed the components of a wireless network and wireless network encryption mechanisms
4
It has discussed the different types of wireless network authentication methods
5
Finally, this module ended with an overview on various wireless network security measures and wireless security tools
6
In the next module, we will discuss on mobile device security in detail
Module Summary